## Slide 1: Introduce Zephyr
Chun-Chieh Li

## Slide 2: Overview
Introduction
Install development environment
Kernel configuration system (Kconfig)
Devicetree

## Slide 3: Introduction (1/3)
Open-source RTOS
  Target connected, resource-constrained, and embedded system
License: Apache 2.0 license
Support architecture: Arm Cortex-M, R, A, Intel x86, RISC-V, ARC, and Xtensa
Support language: C/C++
Support toolchain: Cross GCC for Cortex-M

## Slide 4: Introduction (2/3)
Build system: CMake-based (CMake + Ninja)
Configuration system: Kconfig and Devicetree
  Inherited from Linux kernel but re-implemented in Python for portability to non-Unix OS
West tool, a versatile meta-tool for
  Managing external projects (Git repositories)
  Building projects
  Flashing hardware (pyOCD or OpenOCD)

## Slide 5: Introduction (3/3)
Support development environment
  CLI
    https://docs.zephyrproject.org/latest/develop/getting_started/index.html
  VS Code
    https://github.com/OpenNuvoton/Nuvoton_Tools/blob/master/Documents/VSCode_ZephyrIDE.md
Host environment
  Can develop on Windows, Linux, and macOS
  Git Bash for Windows

## Slide 6: Our ports: Support boards
|-- numaker_gai_m55m1
|-- numaker_m2l31ki
|-- numaker_m3334ki
|-- numaker_m5531
|-- numaker_m55m1
|-- numaker_pfm_m467
`-- numaker_pfm_m487
zephyr/boards/nuvoton/
|-- index.rst
|-- npck3m8k_evb
|-- npcm400_evb
|-- npcx4m8f_evb
|-- npcx7m6fb_evb
|-- npcx9m6f_evb

## Slide 7: Our ports: Support peripherals (1/2)
zephyr/drivers/adc/adc_numaker.c
zephyr/drivers/can/can_numaker.c
zephyr/drivers/clock_control/clock_control_numaker_scc.c
zephyr/drivers/ethernet/eth_numaker.c
zephyr/drivers/flash/soc_flash_numaker.c
zephyr/drivers/flash/soc_flash_numaker_rmc.c
zephyr/drivers/gpio/gpio_numaker.c
zephyr/drivers/hwinfo/hwinfo_numaker.c
zephyr/drivers/hwinfo/hwinfo_numaker_rmc.c
zephyr/drivers/i2c/i2c_numaker.c
zephyr/drivers/misc/ethos_u/ethos_u_numaker.c
zephyr/drivers/pinctrl/pinctrl_numaker.c

## Slide 8: Our ports: Support peripherals (2/2)
zephyr/drivers/pwm/pwm_numaker.c
zephyr/drivers/reset/reset_numaker.c
zephyr/drivers/rtc/rtc_numaker.c
zephyr/drivers/serial/uart_numaker.c
zephyr/drivers/spi/spi_numaker.c
zephyr/drivers/usb/device/usb_dc_numaker.c
zephyr/drivers/usb/udc/udc_numaker.c
zephyr/drivers/usb_c/ppc/usbc_ppc_numaker.c
zephyr/drivers/usb_c/tcpc/ucpd_numaker.c
zephyr/drivers/usb_c/vbus/usbc_vbus_numaker.c
zephyr/drivers/watchdog/wdt_wwdt_numaker.c

## Slide 9: Install development environment
Python (3.10)
  Add into PATH
Git
  Add into PATH
  Git Bash as CLI
CMake (3.20.5) & Ninja
  Add into PATH
Python virtual environment
  $ mkdir zephyrproject
  $ python -m venv zephyrproject/.venv
  $ source zephyrproject/.venv/Scripts/activate

## Slide 10: Install development environment
West
  $ pip install --upgrade west
Example code
  $ unzip -d zephyrproject EC_M55M1_Zephyr_ML_KWS_V1.00.zip
  $ mv zephyrproject/EC_M55M1_Zephyr_ML_KWS_V1.00 zephyrproject/EC_M55M1_Zephyr_ML_KWS
West workspace ‘zephyrproject’
  Manifest repository: EC_M55M1_Zephyr_ML_KWS/west.yml vs. zephyr/west.yml
  $ cd zephyrproject
  $ west init --local EC_M55M1_Zephyr_ML_KWS

## Slide 11: Install development environment
Pull in external dependencies (EC_M55M1_Zephyr_ML_KWS/west.yml)
  $ west update
zephyrproject/
|-- EC_M55M1_Zephyr_ML_KWS
|-- modules
|-- optional
`-- zephyr
zephyrproject/modules/
|-- hal
| |-- cmsis_6
| |-- ethos_u
| `-- nuvoton
`-- lib
|-- cmsis-dsp
`-- cmsis-nn
zephyrproject/optional/
`-- modules
`-- lib
`-- tflite-micro

## Slide 12: Install development environment
Pull in external dependencies (zephyr/west.yml)
  $ west update
zephyrproject/modules/
|-- bsim_hw_models
| `-- nrf_hw_models
|-- crypto
| |-- mbedtls
| `-- tinycrypt
|-- debug
| |-- mipi-sys-t
| |-- percepio
| `-- segger
|-- fs
| |-- fatfs
| `-- littlefs
|-- hal
| |-- adi
| |-- afbr
| |-- altera
| |-- ambiq
| |-- atmel
| |-- bouffalolab
| |-- cmsis
| |-- cmsis_6
| |-- espressif
| |-- ethos_u
| |-- gigadevice
| |-- infineon
| |-- intel
| |-- libmetal
| |-- microchip

## Slide 13: Install development environment
Python dependencies, including pyOCD
  $ west packages pip –install
Zephyr SDK toolchain
  arm-zephyr-eabi vs. arm-none-eabi
  $ west sdk install --install-base toolchains --toolchains arm-zephyr-eabi --no-hosttools
Support pyOCD flash for M55M1
  Download Nuvoton.NuMicroM55_DFP.x.y.z.pack
  Create zephyrproject/pyocd.yaml
pack:
- C:\Users\<USER>\Downloads\Nuvoton.NuMicroM55_DFP.<x.y.z>.pack

## Slide 14: Install development environment
Vela compiler
  $ pip install --upgrade ethos-u-vela
Leave Python virtual environment
  $ deactivate

## Slide 15: Build example code
Enter Python virtual environment
  $ source zephyrproject/.venv/Scripts/activate
Enter West workspace ‘zephyrproject’
  $ cd zephyrproject
Compile
  $ west -v build -b numaker_m55m1 EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS
Flash
  $ west flash
Leave Python virtual environment
  $ deactivate

## Slide 16: Kernal configuration system (Kconfig)
Purpose: Allow to enable, disable, and parameterize software components, drivers, and OS features without having to change any source code
  Can tailor CMake files, C/C++ files, linker script files
Constituent files
  Kconfig* files: Define configuration options (Kconfig symbols)
  *.conf files: Set configuration values (Kconfig fragments)
  .config file: Generated merged configuration file
  autoconf.h: Generated C macro file per above
Kconfig search
  https://docs.zephyrproject.org/latest/kconfig.html

## Slide 17: Kconfig: Define configuration options (1/3)
zephyr/samples/modules/tflite-micro/tflm_ethosu/Kconfig
config TAINT_BLOBS_TFLM
bool
default y
select TAINT_BLOBS
config TAINT_BLOBS_TFLM_ETHOSU
bool "Choose Vela-compiled model targeting Ethos-U"
default y
depends on ETHOS_U_ARM || ETHOS_U_NUMAKER || ETHOS_U_RENESAS
select TAINT_BLOBS_TFLM
zephyr/samples/modules/tflite-micro/tflm_ethosu/src/inference_process.cpp
#ifdef CONFIG_TAINT_BLOBS_TFLM_ETHOSU
...
#else
..
#endif

## Slide 18: Kconfig: Define configuration options (2/3)
zephyr/samples/modules/tflite-micro/tflm_ethosu/Kconfig
config SAMPLE_TFLM_ETHOSU_PMU
bool "Enable PMU counters in sample"
depends on ETHOS_U
help
Enable PMU counters for this sample. When enabled,
the sample collects cycle and selected event counters per inference.
zephyr/samples/modules/tflite-micro/tflm_ethosu/CMakeLists.txt
if(CONFIG_SAMPLE_TFLM_ETHOSU_PMU)
target_sources(app PRIVATE src/ethosu_pmu_monitor.cpp)
...
Endif()

## Slide 19: Kconfig: Define configuration options (3/3)
zephyr/samples/modules/tflite-micro/tflm_ethosu/Kconfig
source "Kconfig.zephyr"
Kconfig include tree
<PROJECT>/Kconfig
zephyr/Kconfig.zephyr
...
zephyr/boards/<VENDOR>/<BOARD>/Kconfig*
...

## Slide 20: Kconfig: Set configuration values (1/3)
Board/SoC specific default (*_defconfig files)
  zephyr/boards/<VENDOR>/<BOARD>/<BOARD>_defconfig
zephyr/boards/nuvoton/numaker_m55m1/numaker_m55m1_defconfig
CONFIG_GPIO=y
# Enable system clock controller driver
CONFIG_CLOCK_CONTROL=y
CONFIG_CLOCK_CONTROL_NUMAKER_SCC=y
# Enable MPU
CONFIG_ARM_MPU=y
CONFIG_SYS_CLOCK_HW_CYCLES_PER_SEC=220000000

## Slide 21: Kconfig: Set configuration values (2/3)
Application specific (*.conf files) (Kconfig fragments)
  <PROJECT>/prj.conf
  <PROJECT>/boards/<BOARD>.conf
zephyr/tests/drivers/i2c/i2c_target_api/prj.conf
CONFIG_LOG=y
CONFIG_I2C_LOG_LEVEL_INF=y
CONFIG_BOOT_BANNER=y
CONFIG_ZTEST=y
CONFIG_I2C=y
CONFIG_I2C_TARGET=y
CONFIG_I2C_EEPROM_TARGET=y
CONFIG_I2C_VIRTUAL=y
zephyr/tests/drivers/i2c/i2c_target_api/boards/numaker_m55m1.conf
CONFIG_I2C=y
CONFIG_I2C_TARGET=y

## Slide 22: Kconfig: Set configuration values (3/3)
CMake cache variables (CONFIG_*)
$ west -v build \
-b numaker_m55m1 \
zephyr/tests/drivers/i2c/i2c_target_api \
-- \
-DCONFIG_SPEED_OPTIMIZATIONS=y

## Slide 23: Kconfig: Generated merged files
Generated combined configuration file
  <BUILD>/zephyr/.config
Generated C header file
  <BUILD>/zephyr/include/generated/zephyr/autoconf.h
  Auto-included via ‘-imacros autoconf.h’

## Slide 24: Common Kconfig options (1/3)
Cache
  CONFIG_CACHE_MANAGEMENT
FPU
  CONFIG_FPU
  CONFIG_FPU_SHARING
  CONFIG_FP_HARDABI
Compiler optimization level
  CONFIG_SIZE_OPTIMIZATIONS (-Os) (default)
  CONFIG_SIZE_OPTIMIZATIONS_AGGRESSIVE (-Oz)
  CONFIG_SPEED_OPTIMIZATIONS (-O2)
  CONFIG_DEBUG_OPTIMIZATIONS (-Og)
  CONFIG_NO_OPTIMIZATIONS (-O0) (stack overflow)

## Slide 25: Common Kconfig options (2/3)
Main stack
  CONFIG_MAIN_STACK_SIZE
Logging
  CONFIG_LOG
  CONFIG_REQUIRES_FLOAT_PRINTF (floating-point)
  CONFIG_LOG_BLOCK_IN_THREAD (few messages dropped)
C++ language
  CONFIG_CPP
  CONFIG_STD_CPP17

## Slide 26: Common Kconfig options (3/3)
CMSIS DSP
  CONFIG_CMSIS_DSP
  CONFIG_CMSIS_DSP_COMPLEXMATH, CONFIG_CMSIS_DSP_FASTMATH, CONFIG_CMSIS_DSP_TRANSFORM, etc.

## Slide 27: Devicetree (1/4)
A hierarchical data structure used to describe H/W and its boot-time configuration
  For system, memory base/size (Flash, SRAM), CPU frequency, etc.
  For peripheral, register base, interrupt, pins, etc.
Unlike Linux, Zephyr parses the DTS at compile time and generates C language macros, rather than blob.
Separate H/W specifics from application logic
  No hardcode
  Retarget without change to C/C++ code

## Slide 28: Devicetree (2/4)
Constituent files
  DTS files (*.dts): Contain board-level definitions and configuration
  DTS include files (*.dtsi): Contain SoC-level or board-level definitions and configurations to be included
  DTS overlay files (*.overlay): Allow customizing or overriding H/W configurations
  DTS binding files (*.yaml): Define which properties are valid within a node and link H/W device to S/W driver

## Slide 29: Devicetree (3/4)
Include tree:
  Board DTS file (--board)
    zephyr/boards/<VENDOR>/<BOARD>/<BOARD>.dts
  Included SoC-level DTSI file (#include)
    Zephyr/dts/arm/nuvoton/<SOC>.dtsi
  Included C header file (#include)
    *.h
  Board overlay file
    <PROJECT>/boards/<BOARD>.overlay
    <PROJECT>/app.overlay

## Slide 30: Devicetree (4/4)
Generated combined DTS file
  <BUILD>/zephyr/zephyr.dts
Generated C macro header file
  build/zephyr/include/generated/zephyr/devicetree_generated.h
  Access via Devicetree API instead of directly
  https://docs.zephyrproject.org/latest/build/dts/api/api.html
Example: DT_N_S_soc_S_serial_4024d000_P_current_speed
  DT_: Common prefix for Devicetree macros
  _S_ : Forward slash ‘/’
  _N_ : Node
  _P_: Property

## Slide 31: Devicetree: System Clock Controller (1/3)
zephyr/dts/arm/nuvoton/m55m1x.dtsi
scc: system-clock-controller@40001000 {
compatible = "nuvoton,numaker-scc";
reg = <0x40001000 0x100>;
#clock-cells = <0>;
lxt = "enable";
hirc48m = "enable";
clk-pclkdiv = <(NUMAKER_CLK_PCLKDIV_PCLK0DIV(2) |
NUMAKER_CLK_PCLKDIV_PCLK1DIV(2) |
NUMAKER_CLK_PCLKDIV_PCLK2DIV(2) |
NUMAKER_CLK_PCLKDIV_PCLK3DIV(2) |
NUMAKER_CLK_PCLKDIV_PCLK4DIV(2))>;
core-clock = <DT_FREQ_M(220)>;
powerdown-mode = <NUMAKER_PMC_SPD0>;

## Slide 32: Devicetree: System Clock Controller (2/3)
zephyr/dts/bindings/clock/nuvoton,numaker-scc.yaml
description: Nuvoton NuMaker System Clock Controller (SCC)
compatible: "nuvoton,numaker-scc"
include: [clock-controller.yaml, base.yaml]
properties:
reg:
required: true
hxt:
type: string
lxt:
type: string
hirc48m:
type: string
clk-pclkdiv:
type: int
core-clock:
type: int

## Slide 33: Devicetree: System Clock Controller (3/3)
zephyr/soc/nuvoton/numaker/m55m1x/soc.c
#if DT_NODE_HAS_PROP(DT_NODELABEL(scc), clk_pclkdiv)
/* Set CLK_PCLKDIV register on request */
CLK->PCLKDIV = DT_PROP(DT_NODELABEL(scc), clk_pclkdiv);
#endif
#if DT_NODE_HAS_PROP(DT_NODELABEL(scc), core_clock)
/* Set core clock (HCLK) on request */
CLK_SetCoreClock(DT_PROP(DT_NODELABEL(scc), core_clock));
#endif

## Slide 34: Devicetree: Peripheral Clock Controller (1/4)
CLK_EnableModuleClock
CLK_SetModuleClock
zephyr/dts/arm/nuvoton/m55m1x.dtsi
uart0: serial@4024d000 {
compatible = "nuvoton,numaker-uart";
reg = <0x4024d000 0x1000>;
interrupts = <75 0>;
resets = <&rst NUMAKER_SYS_UART0RST>;
clocks = <&pcc
NUMAKER_UART0_MODULE
NUMAKER_CLK_UARTSEL0_UART0SEL_HIRC
NUMAKER_CLK_UARTDIV0_UART0DIV(1)>;
};
zephyr/dts/arm/nuvoton/m55m1x.dtsi
scc: system-clock-controller@40001000 {
pcc: peripheral-clock-controller {
compatible = "nuvoton,numaker-pcc";
#clock-cells = <3>;
};

## Slide 35: Devicetree: Peripheral Clock Controller (2/4)
zephyr/dts/bindings/clock/nuvoton,numaker-pcc.yaml
description: Nuvoton NuMaker Peripheral Clock Controller (PCC)
compatible: "nuvoton,numaker-pcc"
include: [clock-controller.yaml, base.yaml]
properties:
"#clock-cells":
const: 3
clock-cells:
- clock-module-index
- clock-source
- clock-divider

## Slide 36: Devicetree: Peripheral Clock Controller (3/4)
zephyr/drivers/serial/uart_numaker.c
Devicetree API
.clk_modidx = DT_INST_CLOCKS_CELL(inst, clock_module_index),
.clk_src = DT_INST_CLOCKS_CELL(inst, clock_source),
.clk_div = DT_INST_CLOCKS_CELL(inst, clock_divider),
Clock Controller API
scc_subsys.pcc.clk_modidx = config->clk_modidx;
scc_subsys.pcc.clk_src = config->clk_src;
scc_subsys.pcc.clk_div = config->clk_div;
clock_control_on(config->clk_dev, (clock_control_subsys_t)&scc_subsys);
clock_control_configure(config->clk_dev, (clock_control_subsys_t)&scc_subsys, NULL);

## Slide 37: Devicetree: Peripheral Clock Controller (4/4)
zephyr/drivers/clock_control/clock_control_numaker_scc.c
static inline int numaker_scc_configure(const struct device *dev, clock_control_subsys_t subsys,
void *data)
{
struct numaker_scc_subsys *scc_subsys = (struct numaker_scc_subsys *)subsys;
if (scc_subsys->subsys_id == NUMAKER_SCC_SUBSYS_ID_PCC) {
SYS_UnlockReg();
CLK_SetModuleClock(scc_subsys->pcc.clk_modidx, scc_subsys->pcc.clk_src,
scc_subsys->pcc.clk_div);
SYS_LockReg();
} else {

## Slide 38: Devicetree: Reset Controller (1/5)
SYS_ResetModule
zephyr/dts/arm/nuvoton/m55m1x.dtsi
uart0: serial@4024d000 {
compatible = "nuvoton,numaker-uart";
reg = <0x4024d000 0x1000>;
interrupts = <75 0>;
resets = <&rst NUMAKER_SYS_UART0RST>;
clocks = <&pcc
NUMAKER_UART0_MODULE
NUMAKER_CLK_UARTSEL0_UART0SEL_HIRC
NUMAKER_CLK_UARTDIV0_UART0DIV(1)>;
};
zephyr/dts/arm/nuvoton/m55m1x.dtsi
rst: reset-controller@40000000 {
compatible = "nuvoton,numaker-rst";
reg = <0x40000000 0x2e0>;
#reset-cells = <1>;
};

## Slide 39: Devicetree: Reset Controller (2/5)
zephyr/dts/bindings/reset/nuvoton,numaker-rst.yaml
description: Nuvoton, Numaker-RESET
compatible: "nuvoton,numaker-rst"
include: [reset-controller.yaml, base.yaml]
properties:
reg:
required: true
"#reset-cells":
const: 1
reset-cells:
- id

## Slide 40: Devicetree: Reset Controller (3/5)
zephyr/drivers/serial/uart_numaker.c
static int uart_numaker_init(const struct device *dev)
{
reset_line_toggle_dt(&config->reset);
}
static const struct uart_numaker_config uart_numaker_cfg_##inst = {
.reset = RESET_DT_SPEC_INST_GET(inst),

## Slide 41: Devicetree: Reset Controller (4/5)
zephyr/drivers/reset/reset_numaker.c
static DEVICE_API(reset, reset_numaker_driver_api) = {
.status = reset_numaker_status,
.line_assert = reset_numaker_line_assert,
.line_deassert = reset_numaker_line_deassert,
.line_toggle = reset_numaker_line_toggle,
};
static const struct reset_numaker_config config = {
.base = (uint32_t)DT_INST_REG_ADDR(0),
};
DEVICE_DT_INST_DEFINE(0, NULL, NULL, NULL, &config, PRE_KERNEL_1,
CONFIG_RESET_INIT_PRIORITY, &reset_numaker_driver_api);

## Slide 42: Devicetree: Reset Controller (5/5)
zephyr/drivers/reset/reset_numaker.
static int reset_numaker_line_assert(const struct device *dev, uint32_t id)
{
sys_set_bit(config->base + NUMAKER_RESET_IP_OFFSET(id), NUMAKER_RESET_IP_BIT(id));
}
static int reset_numaker_line_deassert(const struct device *dev, uint32_t id)
{
sys_clear_bit(config->base + NUMAKER_RESET_IP_OFFSET(id), NUMAKER_RESET_IP_BIT(id));
}
static int reset_numaker_line_toggle(const struct device *dev, uint32_t id)
{
(void)reset_numaker_line_assert(dev, id);
(void)reset_numaker_line_deassert(dev, id);
}

## Slide 43: Devicetree: Pin Controller (1/9)
Pin multi-function (SYS) + partial pin configurations (GPIO)
zephyr/boards/nuvoton/numaker_m55m1/numaker_m55m1.dts
&emac {
pinctrl-0 = <&emac_default>;
pinctrl-names = "default";
status = "okay";
};
zephyr/dts/arm/nuvoton/m55m1x.dtsi
pinctrl: pin-controller@40000080 {
compatible = "nuvoton,numaker-pinctrl";
reg = <0x40000080 0x30 0x40000300 0x100>;
reg-names = "mfos", "mfp";
};

## Slide 44: Devicetree: Pin Controller (2/9)
zephyr/boards/nuvoton/numaker_m55m1/numaker_m55m1-pinctrl.dtsi
&pinctrl {
emac_default: emac_default {
group0 {
pinmux = <PE8MFP_EMAC0_RMII_MDC>,
<PE9MFP_EMAC0_RMII_MDIO>,
<PC8MFP_EMAC0_RMII_REFCLK>,
<PC7MFP_EMAC0_RMII_RXD0>,
<PC6MFP_EMAC0_RMII_RXD1>,
<PA7MFP_EMAC0_RMII_CRSDV>,
<PA6MFP_EMAC0_RMII_RXERR>;
};
group1 {
pinmux = <PE10MFP_EMAC0_RMII_TXD0>,
<PE11MFP_EMAC0_RMII_TXD1>,
<PE12MFP_EMAC0_RMII_TXEN>;
slew-rate = "fast";
};
};
};

## Slide 45: Devicetree: Pin Controller (3/9)
zephyr/dts/bindings/pinctrl/nuvoton,numaker-pinctrl.yaml
compatible: "nuvoton,numaker-pinctrl"
include: base.yaml
properties:
reg:
required: true
child-binding:
child-binding:
include:
- name: pincfg-node.yaml
property-allowlist:
- drive-open-drain
- input-schmitt-enable

## Slide 46: Devicetree: Pin Controller (4/9)
zephyr/dts/bindings/pinctrl/nuvoton,numaker-pinctrl.yaml
child-binding:
child-binding:
properties:
pinmux:
required: true
type: array
drive-strength:
type: string
default: "low"
enum:
- "low"
- "fast"

## Slide 47: Devicetree: Pin Controller (5/9)
zephyr/dts/bindings/pinctrl/nuvoton,numaker-pinctrl.yaml
child-binding:
child-binding:
properties:
slew-rate:
type: string
default: "low"
enum:
- "low"
- "high"
- "fast"
digital-path-disable:
type: boolean

## Slide 48: Devicetree: Pin Controller (6/9)
zephyr/drivers/ethernet/eth_numaker.c
Devicetree API
PINCTRL_DT_INST_DEFINE(0);
static struct eth_numaker_config eth_numaker_cfg_inst = {
.pincfg = PINCTRL_DT_INST_DEV_CONFIG_GET(0),
};
Pin Controller API
static int eth_numaker_init(const struct device *dev)
{
ret = pinctrl_apply_state(cfg->pincfg, PINCTRL_STATE_DEFAULT);
}

## Slide 49: Devicetree: Pin Controller (7/9)
zephyr/drivers/pinctrl/pinctrl_numaker.c
Devicetree API
#define MFP_BASE DT_INST_REG_ADDR_BY_NAME(0, mfp)
#define MFOS_BASE DT_INST_REG_ADDR_BY_NAME(0, mfos)
#define GPA_BASE DT_REG_ADDR(DT_NODELABEL(gpioa))
#define GPIO_SIZE DT_REG_SIZE(DT_NODELABEL(gpioa))
Pin Controller Driver API
int pinctrl_configure_pins(const pinctrl_soc_pin_t *pins, uint8_t pin_cnt, uintptr_t reg)
{
/* Configure all peripheral devices' properties here. */
for (uint8_t i = 0U; i < pin_cnt; i++) {
configure_pin(&pins[i]);
}
return 0;
}

## Slide 50: Devicetree: Pin Controller (8/9)
zephyr/drivers/pinctrl/pinctrl_numaker.c
static void configure_pin(const pinctrl_soc_pin_t *pin)
{
uint32_t *GPx_MFPx = ((uint32_t *)MFP_BASE) + port_index * 4 + (pin_index / 4);
uint32_t *GPx_MFOSx = ((uint32_t *)MFOS_BASE) + port_index;
*GPx_MFPx = (*GPx_MFPx & (~pinMask)) | mfp_cfg;
if (pin->open_drain != 0) {
*GPx_MFOSx |= BIT(pin_index);
} else {
*GPx_MFOSx &= ~BIT(pin_index);
}
gpio_configure(pin, port_index, pin_index);
}

## Slide 51: Devicetree: Pin Controller (9/9)
zephyr/drivers/pinctrl/pinctrl_numaker.c
static void gpio_configure(const pinctrl_soc_pin_t *pin, uint8_t port_idx, uint8_t pin_idx)
{
port = (GPIO_T *)(GPA_BASE + port_idx * GPIO_SIZE);
port->SMTEN = (port->SMTEN & ~BIT(pin_idx)) |
((pin->schmitt_enable ? 1 : 0) << pin_idx);
port->SLEWCTL = (port->SLEWCTL & ~SLEWCTL_MASK(pin_idx)) |
(pin->slew_rate << SLEWCTL_PIN_SHIFT(pin_idx));
port->DINOFF = (port->DINOFF & ~DINOFF_MASK(pin_idx)) |
((pin->digital_disable ? 1 : 0) << DINOFF_PIN_SHIFT(pin_idx));
}

## Slide 52: Devicetree: GPIO (1/3)
zephyr/dts/arm/nuvoton/m2l31x.dtsi
gpioa: gpio@40004000 {
compatible = "nuvoton,numaker-gpio";
gpio-controller;
#gpio-cells = <2>;
reg = <0x40004000 0x40>;
clocks = <&pcc NUMAKER_GPA_MODULE 0 0>;
status = "disabled";
interrupts = <16 2>;
};
zephyr/samples/subsys/usb_c/sink/boards/numaker_m2l31ki.overlay
&tcpc0 {
gpios = <&gpioa 12 0>, <&gpioa 1 GPIO_ACTIVE_HIGH>;
gpio-names = "vbus-detect", "vbus-discharge";
};
&gpioa {
status = "okay";
};

## Slide 53: Devicetree: GPIO (2/3)
zephyr/dts/bindings/gpio/nuvoton,numaker-gpio.yaml
compatible: "nuvoton,numaker-gpio"
include: [gpio-controller.yaml, base.yaml]
properties:
reg:
required: true
"#gpio-cells":
const: 2
gpio-cells:
- pin
- flags

## Slide 54: Devicetree: GPIO (3/3)
zephyr/drivers/usb_c/tcpc/ucpd_numaker.c
Devicetree API
.port = DEVICE_DT_GET(DT_PHANDLE_BY_NAME(node_id, gpios, vbus_detect))
.pin = DT_PHA_BY_NAME(node_id, gpios, vbus_detect, pin)
.dt_flags = DT_PHA_BY_NAME(node_id, gpios, vbus_detect, flags)
GPIO API
gpio_is_ready*
gpio_pin_configure*
Gpio_pin_set*