## Slide 1: M55M1 NPU Keyword Spotting Inference on Zephyr
Chun-Chieh Li

## Slide 2: Overview
Introduce this example code
Optimize model
Introduce Zephyr
Install development environment
Kernel configuration system (Kconfig)
Devicetree

## Slide 3: This example code
Application: Demo machine learning keyword spotting (關鍵詞檢測) inference on Zephyr
MCU: M55M1
  NPU
  DMIC
OS: Zephyr
Board: NuMaker-X-M55M1D
M55M1 BSP KeywordSpotting: https://github.com/OpenNuvoton/M55M1BSP/tree/master/SampleCode/MachineLearning/KeywordSpotting
Download: [M55M1] NPU Keyword Spotting Inference - MCU BSP & Example Code | Nuvoton NuForum

## Slide 4: Software development flow
Cortex-M CPU
PC
Trained and quantized model
Vela
Vela-compiled model
User app
TensorFlow Lite Micro
Ethos-U driver
CMSIS-NN kernels
Ref kernels
Command stream
Ethos-U NPU

## Slide 5: Directory structure
zephyrproject | 
EC_M55M1_Zephyr_ML_KWS | 
Library | 
StdDriver | Zephyr build system files to pull in lacking peripheral driver header and source files
SampleCode | 
ExampleCode | 
Zephyr_ML_KWS | Source files of example code
ThirdParty | 
ml-embedded-evaluation-kit | Inference preprocessing/postprocessing header and source files
zephyr | Zephyr module YAML file

## Slide 6: Application control flow
Record audio clip via DMIC
Preprocess recorded audio (MFCC) clip to specified input tensor format for inference
Run keyword spotting inference
Postprocess output tensor format usable by external applications
Initialize platform, drivers, TFLM, etc.
Zephyr: MPU, UART, GPIO, NPU
Non-OS: DMIC

## Slide 7: Demo result
Host terminal program: 115200/8-N-1
Steps
  Type ‘kws resume’
  Speak trained keyword like ‘Go’
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/src/Model/Labels.cpp
"yes", "no", "up", "down", "left", "right", "on", "off", "stop", "go",

## Slide 8: Optimize the model (1/3)
Download DS-CNN Medium INT8 model
  Original model: ds_cnn_m_quantized.tflite
  https://github.com/Arm-Examples/ML-zoo/tree/master/models/keyword_spotting/ds_cnn_medium/model_package_tf/model_archive/TFLite/tflite_int8
Optimize using Vela
  $ vela ds_cnn_m_quantized.tflite --output-dir . --accelerator-config ethos-u55-256 --optimise Performance
  Optimized model: ds_cnn_m_quantized_vela.tflite
  Bit-accurate

## Slide 9: Optimize the model (2/3)
Netron
https://netron.app/

## Slide 10: Optimize the model (3/3)
Match Ethos-U NPU config among:
  Ethos-U RTL config: For M55M1, Ethos-U55, 256 macs_per_cycle
  Vela command line: --accelerator-config ethos-u55-256
  Ethos-U core driver config (ETHOSU_TARGET_NPU_CONFIG): "ethos-u55-256"

## Slide 11: Introduce Zephyr (1/3)
Open-source RTOS
  Target connected, resource-constrained, and embedded system
License: Apache 2.0 license
Support architecture: Arm Cortex-M, R, A, Intel x86, RISC-V, ARC, and Xtensa
Support language: C/C++
Support toolchain: Cross GCC for Cortex-M

## Slide 12: Introduce Zephyr (2/3)
Build system: CMake-based (CMake + Ninja)
Configuration system: Kconfig and Devicetree
  Inherited from Linux kernel but re-implemented in Python for portability to non-Unix OS
West tool, a versatile meta-tool for
  Managing external projects (Git repositories)
  Building projects
  Flashing hardware (pyOCD or OpenOCD)

## Slide 13: Introduce Zephyr (3/3)
Support development environment
  CLI
    https://docs.zephyrproject.org/latest/develop/getting_started/index.html
  VS Code
    https://github.com/OpenNuvoton/Nuvoton_Tools/blob/master/Documents/VSCode_ZephyrIDE.md
Host environment
  Can develop on Windows, Linux, and macOS
  Git Bash for Windows

## Slide 14: Install development environment (1/6)
Python (3.10)
  Add into PATH
Git
  Add into PATH
  Git Bash as CLI
CMake (3.20.5) & Ninja
  Add into PATH
Python virtual environment
  $ mkdir zephyrproject
  $ python -m venv zephyrproject/.venv
  $ source zephyrproject/.venv/Scripts/activate

## Slide 15: Install development environment (2/6)
West
  $ pip install --upgrade west
Example code
  $ unzip -d zephyrproject EC_M55M1_Zephyr_ML_KWS_V1.00.zip
  $ mv zephyrproject/EC_M55M1_Zephyr_ML_KWS_V1.00 zephyrproject/EC_M55M1_Zephyr_ML_KWS
West workspace ‘zephyrproject’
  Manifest repository: EC_M55M1_Zephyr_ML_KWS/west.yml vs. zephyr/west.yml
  $ cd zephyrproject
  $ west init --local EC_M55M1_Zephyr_ML_KWS

## Slide 16: Install development environment (3/6)
Pull in external dependencies (EC_M55M1_Zephyr_ML_KWS/west.yml)
  $ west update
zephyrproject/
|-- EC_M55M1_Zephyr_ML_KWS
|-- modules
|-- optional
`-- zephyr
zephyrproject/modules/
|-- hal
| |-- cmsis_6
| |-- ethos_u
| `-- nuvoton
`-- lib
|-- cmsis-dsp
`-- cmsis-nn
zephyrproject/optional/
`-- modules
`-- lib
`-- tflite-micro

## Slide 17: Install development environment (4/6)
Pull in external dependencies (zephyr/west.yml)
  $ west update
zephyrproject/modules/
|-- bsim_hw_models
| `-- nrf_hw_models
|-- crypto
| |-- mbedtls
| `-- tinycrypt
|-- debug
| |-- mipi-sys-t
| |-- percepio
| `-- segger
|-- fs
| |-- fatfs
| `-- littlefs
|-- hal
| |-- adi
| |-- afbr
| |-- altera
| |-- ambiq
| |-- atmel
| |-- bouffalolab
| |-- cmsis
| |-- cmsis_6
| |-- espressif
| |-- ethos_u
| |-- gigadevice
| |-- infineon
| |-- intel
| |-- libmetal
| |-- microchip

## Slide 18: Install development environment (5/6)
Python dependencies, including pyOCD
  $ west packages pip –install
Zephyr SDK toolchain
  arm-zephyr-eabi vs. arm-none-eabi
  $ west sdk install --install-base toolchains --toolchains arm-zephyr-eabi --no-hosttools
Support pyOCD flash for M55M1
  Download Nuvoton.NuMicroM55_DFP.x.y.z.pack
  Create zephyrproject/pyocd.yaml
pack:
- C:\Users\<USER>\Downloads\Nuvoton.NuMicroM55_DFP.<x.y.z>.pack

## Slide 19: Install development environment (6/6)
Vela compiler
  $ pip install --upgrade ethos-u-vela
Exit Python virtual environment
  $ deactivate

## Slide 20: Build this example code
Enter Python virtual environment
  $ source zephyrproject/.venv/Scripts/activate
Enter West workspace ‘zephyrproject’
  $ cd zephyrproject
Compile
  $ west -v build -b numaker_m55m1 EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS
Flash
  $ west flash
Exit Python virtual environment
  $ deactivate

## Slide 21: Kernal configuration system (Kconfig)
Purpose: Allow to enable, disable, and parameterize software components, drivers, and OS features without having to change any source code
  Can tailor CMake files, C/C++ files, linker script files
Constituent files
  Kconfig* files: Define configuration options (Kconfig symbols)
  *.conf files: Set configuration values (Kconfig fragments)
  .config file: Generated merged configuration file
  autoconf.h: Generated C macro file per above

## Slide 22: Kconfig: Search
Kconfig search
  https://docs.zephyrproject.org/latest/kconfig.html

## Slide 23: Kconfig: Generated merged files (1/2)
Generated combined configuration file
  build/zephyr/.config
build/zephyr/.config
CONFIG_NVT_ML_REQUIRES_ETHOS_U=y
CONFIG_NVT_ML_TFLM_TENSOR_ARENA_SIZE=280000
CONFIG_NVT_ML_KWS_INPUT_DMIC=y
# CONFIG_NVT_ML_KWS_INPUT_WAVE_BLOB is not set
CONFIG_NVT_ML_REQUIRES_KWS_MODEL_DS_CNN_M_QUANTIZED=y
CONFIG_NVT_ML_KWS_MODEL_DS_CNN_M_QUANTIZED_ETHOS_U55_256_SPEED=y
# CONFIG_INPUT is not set
# CONFIG_WIFI is not set
# CONFIG_REGULATOR is not set
CONFIG_SYSTEM_WORKQUEUE_STACK_SIZE=1024
CONFIG_MAIN_STACK_SIZE=4096

## Slide 24: Kconfig: Generated merged files (2/2)
Generated C header file
  build/zephyr/include/generated/zephyr/autoconf.h
  Auto-included via ‘-imacros autoconf.h’
build/zephyr/include/generated/zephyr/autoconf.h
#define CONFIG_NVT_ML_REQUIRES_ETHOS_U 1
#define CONFIG_NVT_ML_TFLM_TENSOR_ARENA_SIZE 280000
#define CONFIG_NVT_ML_KWS_INPUT_DMIC 1
#define CONFIG_NVT_ML_REQUIRES_KWS_MODEL_DS_CNN_M_QUANTIZED 1
#define CONFIG_NVT_ML_KWS_MODEL_DS_CNN_M_QUANTIZED_ETHOS_U55_256_SPEED 1
#define CONFIG_SYSTEM_WORKQUEUE_STACK_SIZE 1024
#define CONFIG_MAIN_STACK_SIZE 4096

## Slide 25: Kconfig: Define config options (1/3)
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/Kconfig:
config NVT_ML_TFLM_TENSOR_ARENA_SIZE
int "TFLM tensor arena size"
default 280000
help
Define TFLM tensor arena size

## Slide 26: Kconfig: Define config options (2/3)
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/Kconfig:
choice NVT_ML_KWS_INPUT_CHOICE
prompt "Choose ML keyword spotting input source"
default NVT_ML_KWS_INPUT_DMIC if BOARD_NUMAKER_M55M1
default NVT_ML_KWS_INPUT_WAVE_BLOB
config NVT_ML_KWS_INPUT_DMIC
bool "DMIC as KWS input"
help
Use digital microphone as keyword spotting input
config NVT_ML_KWS_INPUT_WAVE_BLOB
bool "Wave blob as KWS input"
help
Use embedded wave blob as keyword spotting input
endchoice

## Slide 27: Kconfig: Define config options (3/3)
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/Kconfig:
choice NVT_ML_KWS_MODEL_CHOICE
prompt "Choose ML keyword spotting model"
default NVT_ML_KWS_MODEL_DS_CNN_M_QUANTIZED_ETHOS_U55_256_SPEED
config NVT_ML_KWS_MODEL_DS_CNN_M_QUANTIZED_ETHOS_U55_256_SPEED
bool "DS-CNN Medium KWS model, vela-compile for speed"
select NVT_ML_REQUIRES_ETHOS_U
select NVT_ML_REQUIRES_KWS_MODEL_DS_CNN_M_QUANTIZED
help
Use DS-CNN Medium keyword spotting model, type INT8,
vela-compile for Ethos-U55/256 MAC, optimize for speed
endchoice

## Slide 28: Kconfig: Set config values (1/3)
Cache
  CONFIG_CACHE_MANAGEMENT
FPU
  CONFIG_FPU
  CONFIG_FPU_SHARING
  CONFIG_FP_HARDABI
Compiler optimization level
  CONFIG_SIZE_OPTIMIZATIONS (-Os) (default)
  CONFIG_SIZE_OPTIMIZATIONS_AGGRESSIVE (-Oz)
  CONFIG_SPEED_OPTIMIZATIONS (-O2)
  CONFIG_DEBUG_OPTIMIZATIONS (-Og)
  CONFIG_NO_OPTIMIZATIONS (-O0) (stack overflow)
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/prj.conf
CONFIG_CACHE_MANAGEMENT=y
CONFIG_FPU=y
CONFIG_FPU_SHARING=y
CONFIG_FP_HARDABI=y
CONFIG_SPEED_OPTIMIZATIONS=y

## Slide 29: Kconfig: Set config values (2/3)
Main stack
  CONFIG_MAIN_STACK_SIZE
Logging
  CONFIG_LOG
  CONFIG_REQUIRES_FLOAT_PRINTF (floating-point)
  CONFIG_LOG_BLOCK_IN_THREAD (few messages dropped)
C++ language
  CONFIG_CPP
  CONFIG_STD_CPP17
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/prj.conf
CONFIG_MAIN_STACK_SIZE=4096
CONFIG_LOG=y
CONFIG_REQUIRES_FLOAT_PRINTF=y
CONFIG_LOG_BLOCK_IN_THREAD=y
CONFIG_CPP=y
CONFIG_STD_CPP17=y

## Slide 30: Kconfig: Set config values (3/3)
CMSIS DSP
  CONFIG_CMSIS_DSP
  CONFIG_CMSIS_DSP_COMPLEXMATH, CONFIG_CMSIS_DSP_FASTMATH, CONFIG_CMSIS_DSP_TRANSFORM, etc.
Shell
  CONFIG_SHELL (kws resume, kws suspend, etc.)
TensorFlow Lite Micro & Ethos-U
  CONFIG_TENSORFLOW_LITE_MICRO
  CONFIG_ETHOS_U
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/prj.conf
CONFIG_CMSIS_DSP=y
CONFIG_CMSIS_DSP_COMPLEXMATH=y
CONFIG_CMSIS_DSP_FASTMATH=y
CONFIG_CMSIS_DSP_TRANSFORM=y
CONFIG_SHELL=y
CONFIG_TENSORFLOW_LITE_MICRO=y

## Slide 31: Devicetree
A hierarchical data structure used to describe H/W and its boot-time configuration
  For system, memory base/size (Flash, SRAM), CPU frequency, etc.
  For peripheral, register base, interrupt, pins, etc.
Unlike Linux kernel, Zephyr parses the DTS at compile time and generates C language macros, rather than blob.
Separate H/W specifics from application logic
  No hardcode
  Retarget without change to C/C++ code

## Slide 32: Devicetree: Constituent files
DTS files (*.dts): Contain board-level definitions and configuration
DTS include files (*.dtsi): Contain SoC-level or board-level definitions and configurations to be included
DTS overlay files (*.overlay): Allow customizing or overriding H/W configurations
DTS binding files (*.yaml): Define which properties are valid within a node and link H/W device to S/W driver

## Slide 33: Devicetree: Binding
zephyr/dts/arm/nuvoton/m55m1h2l.dtsi:
npu0: npu@40003000 {
compatible = "nuvoton,numaker-npu";
reg = <0x40003000 0x1000>;
interrupts = <13 0>;
resets = <&rst NUMAKER_SYS_NPURST>;
clocks = <&pcc NUMAKER_NPU0_MODULE 0 0>;
secure-enable;
privilege-enable;
status = "disabled";
};
zephyr/dts/bindings/arm/nuvoton,numaker-npu.yaml:
compatible: "nuvoton,numaker-npu"
include: ["arm,ethos-u.yaml", reset-device.yaml]
properties:
reg:
required: true
interrupts:
required: true
resets:
required: true
clocks:
required: true
zephyr/dts/bindings/arm/arm,ethos-u.yaml:
compatible: "arm,ethos-u"
include: base.yaml
properties:
reg:
required: true
interrupts:
required: true
secure-enable:
type: boolean
privilege-enable:
type: boolean
fast-memory-region:
type: phandle
zephyr/drivers/misc/ethos_u/ethos_u_numaker.c:
#define DT_DRV_COMPAT nuvoton_numaker_npu

## Slide 34: Devicetree: Include tree (1/2)
Board DTS file (--board)
  zephyr/boards/<VENDOR>/<BOARD>/<BOARD>.dts
Included SoC-level DTSI file (#include)
  zephyr/dts/arm/nuvoton/<SOC>.dtsi
Included C header file (#include)
  *.h
zephyr/boards/nuvoton/numaker_m55m1/numaker_m55m1.dts
#include <nuvoton/m55m1h2l.dtsi>
#include "numaker_m55m1-pinctrl.dtsi"
#include <zephyr/dt-bindings/input/input-event-codes.h>

## Slide 35: Devicetree: Include tree (2/2)
Board overlay file
  <PROJECT>/boards/<BOARD>.overlay
  <PROJECT>/app.overlay
EC_M55M1_Zephyr_ML_KWS/SampleCode/ExampleCode/Zephyr_ML_KWS/boards/numaker_m55m1.overlay
&npu0 {
status = "okay";
};
&gpiob {
status = "okay";
};

## Slide 36: Devicetree: Generated files (1/2)
Combined DTS file
  build/zephyr/zephyr.dts
build/zephyr/zephyr.dts
/soc/npu@40003000
/ {
soc {
npu0: npu@40003000 {
compatible = "nuvoton,numaker-npu";
reg = < 0x40003000 0x1000 >;
interrupts = < 0xd 0x0 >;
resets = < &rst 0x400006 >;
c locks = < &pcc 0x3d 0x0 0x0 >;
secure-enable;
privilege-enable;
status = "okay";
};

## Slide 37: Devicetree: Generated files (2/2)
C macro header file
  build/zephyr/include/generated/zephyr/devicetree_generated.h
build/zephyr/include/generated/zephyr/devicetree_generated.h
/soc/npu@40003000
/*
* Devicetree node: /soc/npu@40003000
*/
/* Node's full path: */
#define DT_N_S_soc_S_npu_40003000_PATH "/soc/npu@40003000"
/* Node's name with unit-address: */
#define DT_N_S_soc_S_npu_40003000_FULL_NAME "npu@40003000"
#define DT_N_S_soc_S_npu_40003000_FULL_NAME_UNQUOTED npu@40003000
#define DT_N_S_soc_S_npu_40003000_FULL_NAME_TOKEN npu_40003000

## Slide 38: Devicetree: How to access (1/2)
build/zephyr/zephyr.dts
/ {
soc {
npu0: npu@40003000 {
compatible = "nuvoton,numaker-npu";
reg = < 0x40003000 0x1000 >;
interrupts = < 0xd 0x0 >;
… };
};
};
build/zephyr/include/generated/zephyr/devicetree_generated.h
#define DT_N_S_soc_S_npu_40003000_P_reg {1073754112 /* 0x40003000 */, 4096 /* 0x1000 */}
Decode generated C macro
  DT_: Common prefix for Devicetree macros
  _S_ : Forward slash ‘/’
  _N_ : Node
  _P_: Property

## Slide 39: Devicetree: How to access (2/2)
Can be accessed by driver, subsystem, or user application
Access via Devicetree API instead of directly
zephyr/drivers/misc/ethos_u/ethos_u_numaker.c
static const struct ethos_u_numaker_config ethos_u_numaker_config_##inst = {
.base_addr = (void *)DT_INST_REG_ADDR(inst),
.clkctrl_dev = DEVICE_DT_GET(DT_PARENT(DT_INST_CLOCKS_CTLR(inst))),
.pcc = NUMAKER_PCC_INST_GET(inst),
.reset = RESET_DT_SPEC_INST_GET(inst),
.irq_config = ethos_u_numaker_irq_config_##inst,
.secure_enable = DT_INST_PROP(inst, secure_enable),
.privilege_enable = DT_INST_PROP(inst, privilege_enable),
};