## Slide 1: Integrate M55M1 Ethos-U NPU with Zephyr
MS30 李俊杰
4/29/2025

## Slide 2: Overview
Software development flow
Model replacement and verification
Ethos-U driver porting guide

## Slide 3: Software development flow
Cortex-M CPU
PC
Trained and quantized model
Vela
Vela-compiled model
User app
TensorFlow Lite Micro
Ethos-U driver
CMSIS-NN kernels
Ref kernels
Command stream
Ethos-U NPU

## Slide 4: Software environment
Zephyr west
Vela
  pip install ethos-u-vela
TensorFlow Lite Micro
  Optional zephyr module
  west config manifest.project-filter -- +tflite-micro; west update
Ethos-U core driver
  Default zephyr module
  west update

## Slide 5: Download trained model
Arm Model Zoo
Example: keyword_spotting_cnn_small_int8
  Model: cnn_s_quantized.tflite
  Input: testing_input/input/0.npy
  Output: testing_output/identity/0.npy

## Slide 6: Compile model with Vela
Compile targeting M55M1 NPU (Ethos-U55, 256 macs_per_cycle)
  vela cnn_s_quantized.tflite --output-dir . --accelerator-config ethos-u55-256
  Original model: cnn_s_quantized.tflite, run entirely by CPU
  Vela-compiled model: cnn_s_quantized_vela.tflite, run by Ethos-U and CPU
  Bit-accurate: same input/output apply to both models

## Slide 7: Replace model/input/output (1/2)
Convert model/input/output to C array from binary
  xxd -c 16 -i cnn_s_quantized.tflite cnn_s_quantized.tflite.h
  xxd -c 16 -i cnn_s_quantized_vela.tflite cnn_s_quantized_vela.tflite.h
  xxd -c 16 -i testing_input/input/0.npy testing_input/input/0.npy.h
  xxd -c 16 -i testing_output/identity/0.npy testing_output/identity/0.npy.h

## Slide 8: Replace model/input/output (2/2)
Replace into zephyr tflm_ethosu sample
  Sample: zephyr/samples/modules/tflite-micro
  cnn_s_quantized_vela.tflite.h  keyword_spotting_cnn_small_int8_ethos_u55_256/model.h
  testing_input/input/0.npy.h  keyword_spotting_cnn_small_int8_ethos_u55_256/input.h
  testing_output/identity/0.npy.h  keyword_spotting_cnn_small_int8_ethos_u55_256/output.h
Note for input/output, the first 128 bytes are header and don’t copy to sample

## Slide 9: Sample: tflm_ethosu (1/3)
Model
  Locate at section .rodata.tflm_model
  Require 16-byte aligned
Tensor arena (NPU buffer)
  Locate at section .noinit.tflm_arena
  Require Cache line aligned (32-byte aligned)
  Override Ethos-U dcache flush/invalidate
    ethosu_flush_dcache
    ethosu_invalidate_dcache
Input/Output
  No special allocation requirement because they will copy to/from above tensor arena

## Slide 10: Sample: tflm_ethosu (2/3)
Build with Ethos-U
  west -v build -b numaker_m55m1 zephyr/samples/modules/tflite-micro/tflm_ethosu
Build without Ethos-U
  west -v build -b numaker_m55m1 zephyr/samples/modules/tflite-micro/tflm_ethosu -DCONFIG_TAINT_BLOBS_TFLM_ETHOSU=n

## Slide 11: Sample: tflm_ethosu (3/3)

## Slide 12: Ethos-U zephyr driver
In-tree
Zephyr frontend of Ethos-U core driver
  Devicetree binding file
    Data cache flush
    Data cache invalidate
  Devicetree node
  Driver source

## Slide 13: Ethos-U core driver
Zephyr external module
  Its Arm source
Match Ethos-U NPU config
  For M55M1, ethos-u55, 256 macs_per_cycle
Match Ethos-U NPU config among:
Ethos-U RTL config
Vela command line
Ethos-U core driver config

## Slide 14
Thank You